## Slide 1
5/30
Ch 13 – Embedded Systems
NEU - 2016

## Slide 2: Embedded System
Refers to the use of electronics and software within a product that is designed to perform a dedicated function
    Part of a larger system or product
    Mechanical/electrical
    E.g., antilock braking system, smart home components, etc.
Notes: The term embedded system refers to the use of electronics and software within a
product, as opposed to a general-purpose computer, such as a laptop or desktop
system. The following is a good general definition:
Embedded system : A combination of computer hardware and software, and
perhaps additional mechanical or other parts, designed to perform a dedicated
function. In many cases, embedded systems are part of a larger system or product,
as in the case of an antilock braking system in a car.
Often, embedded systems are tightly coupled to their environment. This can
give rise to real-time constraints imposed by the need to interact with the environment.
Constraints, such as required speeds of motion, required precision of measurement,
and required time durations, dictate the timing of software operations.
If multiple activities must be managed simultaneously, this imposes more complex
real-time constraints.

## Slide 3
Notes: Figure 13.1, based on [KOOP96], shows in general terms an embedded system
organization. In addition to the processor and memory, there are a number of elements
that differ from the typical desktop or laptop computer:
• There may be a variety of interfaces that enable the system to measure, manipulate,
and otherwise interact with the external environment.
• The human interface may be as simple as a flashing light or as complicated as
real-time robotic vision.
• The diagnostic port may be used for diagnosing the system that is being controlled—
not just for diagnosing the embedded computer.
• Special-purpose field programmable (FPGA), application specific (ASIC), or
even nondigital hardware may be used to increase performance or safety.
• Software often has a fixed function and is specific to the application.

## Slide 4: Characteristics of Embedded OS
Real-time operation
Reactive operation
Configurability
I/O device flexibility
Streamlined protection mechanisms
Direct use of interrupts
Notes: A simple embedded system, with simple functionality, may be controlled by a
special-purpose program or set of programs with no other software. Typically,
more complex embedded systems include an OS. Although it is possible in
principle to use a general-purpose OS, such as Linux, for an embedded system,
constraints of memory space, power consumption, and real-time requirements
typically dictate the use of a special-purpose OS designed for the embedded
system environment.
The following are some of the unique characteristics and design requirements
for embedded operating systems:
• Real-time operation: In many embedded systems, the correctness of a computation
depends, in part, on the time at which it is delivered. Often, real-time
constraints are dictated by external I/O and control stability requirements.
• Reactive operation: Embedded software may execute in response to external
events. If these events do not occur periodically or at predictable intervals, the
embedded software may need to take into account worst-case conditions and
set priorities for execution of routines.
• Configurability: Because of the large variety of embedded systems, there is
a large variation in the requirements, both qualitative and quantitative, for
embedded OS functionality. Thus, an embedded OS intended for use on a
variety of embedded systems must lend itself to flexible configuration so that
only the functionality needed for a specific application and hardware suite is
provided. [MARW06] gives the following examples. The linking and loading
functions can be used to select only the necessary OS modules to load.
Conditional compilation can be used. If an object-oriented structure is used,
proper subclasses can be defined. However, verification is a potential problem
for designs with a large number of derived tailored operating systems.
Takada cites this as a potential problem for eCos [TAKA01].
• I/O device flexibility: There is virtually no device that needs to be supported
by all versions of the OS, and the range of I/O devices is large. [MARW06]
suggests that it makes sense to handle relatively slow devices such as disks and
network interfaces by using special tasks instead of integrating their drives into
the OS kernel.
Streamlined protection mechanisms: Embedded systems are typically designed
for a limited, well-defined functionality. Untested programs are rarely added
to the software. After the software has been configured and tested, it can be
assumed to be reliable. Thus, apart from security measures, embedded systems
have limited protection mechanisms. For example, I/O instructions need
not be privileged instructions that trap to the OS; tasks can directly perform
their own I/O. Similarly, memory protection mechanisms can be minimized.
[MARW06] provides the following example. Let switch correspond to the
memory-mapped I/O address of a value that needs to be checked as part of an
I/O operation. We can allow the I/O program to use an instruction such as load
register , switch to determine the current value. This approach is preferable
to the use of an OS service call, which would generate overhead for saving
and restoring the task context.
• Direct use of interrupts: General-purpose operating systems typically do not
permit any user process to use interrupts directly. [MARW06] lists three
reasons why it is possible to let interrupts directly start or stop tasks (e.g., by
storing the task’s start address in the interrupt vector address table) rather than
going through OS interrupt service routines: (1) Embedded systems can be
considered to be thoroughly tested, with infrequent modifications to the OS or
application code; (2) protection is not necessary, as discussed in the preceding
bullet item; and (3) efficient control over a variety of devices is required.

## Slide 5: Developing an Embedded OS
Two general approaches:
  Adapt existing OS
    Familiar interface
    Integration with existing development
  Design and implement specific OS
    Fast & lightweight
    Handles interrupts and realtime interaction
Two examples are:
eCos
TinyOS
Notes: There are two general approaches to developing an embedded OS.
  The first approach is to take an existing OS and adapt it for the embedded application.
  The other approach is to design and implement an OS intended solely for embedded use
A significant number of operating systems have been designed from the ground up
for embedded applications. Two prominent examples of this latter approach are
eCos and TinyOS, both of which are discussed in this chapter.
Typical characteristics of a specialized embedded OS include the following:
• Has a fast and lightweight process or thread switch
• Scheduling policy is real time and dispatcher module is part of scheduler
instead of separate component.
• Has a small size
• Responds to external interrupts quickly; typical requirement is response time
of less than 10 μs
• Minimizes intervals during which interrupts are disabled
• Provides fixed or variable-sized partitions for memory management as well as
the ability to lock code and data in memory
• Provides special sequential files that can accumulate data at a fast rate

## Slide 6: Embedded Linux
A version of Linux running in an embedded system
  an embedded Linux kernel will be far smaller than an ordinary Linux kernel
Typically tailored to a specific set of devices, periphrals, and protocols, depending on hardware
Cross-Compiling
  Allows for compiling of the OS distribution on hardware other than the host system
Notes: The term embedded Linux simply means a version of Linux running in an embedded
system. In this section, we highlight some of the key differences between embedded
Linux and a version of Linux running on a desktop or laptop computer.
Desktop and server Linux systems need to support a large number of devices because
of the wide variety of configurations that use Linux. Similarly, such systems
also need to support a range of communication and data exchange protocols so that
they can be used for a large number of different purposes. Embedded devices typically
require support for a specific set of devices, peripherals, and protocols, depending
on the hardware that is present in a given device and the intended purpose of
that device. Fortunately, the Linux kernel is highly configurable in terms of the architecture
that it is compiled for and the processors and devices that it supports.
An embedded Linux distribution is a version of Linux to be customized for
the size and hardware constraints of embedded devices, and includes software packages
that support a variety of services and applications on those devices. Thus, an
embedded Linux kernel will be far smaller than an ordinary Linux kernel.

## Slide 7: Advantages of Embedded Linux
Open source
  Vendor/hardware independence (not relying on proprietary updates)
  Vast hardware support (processors/architectures/peripherals)
Low cost
Familiarity/Usability
Notes: Embedded versions of Linux began to appear as early as 1999. A number of companies
have developed their own versions tailored to specific platforms. Advantages of
using Linux as the basis for an embedded OS include the following:
• Vendor independence: The platform provider is not dependent on a particular
vendor to provide needed features and meet deadlines for deployment.
• Varied hardware support: Linux support for a wide range of processor architectures
and peripheral devices makes it suitable for virtually any embedded
system.
• Low cost: The use of Linux minimizes cost for development and training.
• Open source: The use of Linux provides all of the advantages of open source
software.

## Slide 8: Embedded Linux?
Android (Phones)
MST ACM SIG-Security talk
  Building your own hardened router
    COTS hardware
    “Embedded Linux” (minimal Debian)